## Slide 1
Logel User Guide
TOOL

## Slide 2
Quick view
Quick start to capture log
Quick start to play log file
Capture Setting
Parser Setting
Views
Search
Bookmark
Window management
Filter
Tools
Toolbar
Status bar
CMD Parameters
Table of Contents

## Slide 3: Quick View
Tool Version
Modem Version

## Slide 4: Quick start to capture log
Click button on the toolbar to capture log，it will change to if successfully
  Logel Tool connects to device by UART type
  Logel Tool can auto identify the port by default
  Notice:
  If you did not use SPRD drivers, maybe the port name is not identified by Logel Tool,
  so you need to select right ports in Capture Setting window before clicking button

## Slide 5: Quick start to play log file
Play .logel/.lst/.log file
  Click button on the toolbar to open log file, it will change to if successfully

## Slide 6: Capture Setting
Click Button on the toolbar to show capture setting
Capture Settings
Log Dir: set the log files output folder
Type UART：
  Diag port：used to communicate with device
  Log port： only used to receive log data
  Log Pt Capture Only: used to capture and save to file
  usually used to capture WCN log raw data to a file.
  AGDSP Port: only used to receive AG DSP log data
  Common TP Port: use to receive DSP raw data by UART
  LTE TP Port: use to receive DSP raw data by UART
  TG TP Port: use to receive DSP raw data by UART
  Power Trace Port: use to receive power trace data by UART
  Auto Identify Port: switch to manual or auto identify ports
  Type Channel-Server(Simba)：
  Set Address(IP) and Port to connect to Channel-Server tool or Simba tool, using Socket protocol encapsulated DIAG packet without 7E header and tail, no escape byte.
  Type Socket:
  Set Address(IP) and Port to connect to simulator, using Socket protocol encapsulated DIAG packet
  Type FILE:
  Open one or more .log files to replay

## Slide 7: Capture Setting – Port Notice
Type | Name | Protocol | Notice
DIAG | SPRD LTE DIAG | DIAG | Communicate with modem and output modem dump data when modem assert
 | SPRD DIAG(SENSOR HUB) | DIAG | Communicate with modem and output modem log if no SPRD LTE DIAG device
 | SPRD U2S DIAG | DIAG | Communicate with device in calibration mode
 | SPRD WCN DIAG(LOG) | DIAG | Communicate with WCN modem
LOG | SPRD LTE LOG | SMP | Output PS and DSP log of Modem
 | SPRD WCN DIAG(LOG) | SMP | Output WIFI Trace and BT DSP log of WCN Modem
 | SPRD U2S DIAG | SMP | Output system dump files using SMP protocol in System Dump mode,
 | SPRD LOG(AGDSP) | SMP | Output AGDSP data such as TP, Audio, IQ, mem.
AT | SPRD LTE AT(WIQ) | AT | Communicate with Modem by AT command
 | SPRD AT | AT | Communicate with Modem by AT command if no SPRD LTE AT device shows
 | SPRD WCN AT | AT | Communicate with WCN modem by AT command
UART | USB SERIAL PORT | RAW | Output raw data such as DSP, Power Trace data
 | SPRD LTE AT(WIQ) | RAW | Output WIQ raw data in WIQ mode, only for old projects who have no SPRD IQ device
 | SPRD IQ | RAW | Output WIQ raw data, and only show in WIQ mode
Download | SPRD U2S DIAG | Boot Mode | Burn SW files to flash using boot-mode protocol in download mode

## Slide 8: Parser Setting
Click menu Option->Parser Settings
Auto Loading Default Parser:
  Tool will find parser and load the matched parser,
  search order:
    Bin\Parser
    Search Path
    Parser Server
    Device
  If no matched parser used Bin\Parser with the Logel
  Search Path: the local parsers folder storing parsers.
Parser Lib Dir:
  Specify a parser folder to decode the log
Database file:
  Set the parser got from YLOG, such as modem_db.gz
Notice:
  Parser is very import to decode the log.
  Make sure the parser is matched with the modem version.
  You can find the parser in the project release package, under the Logel tool bin\Parser folder.

## Slide 9: [View] Internal Messages(1)
Three sub windows in this frame
  Top is message list
  Middle is message content: LOCAL & PEER
  Bottom is message raw data : LOCAL & PEER
Message content menu
  Select All: Select all items this tree
  Select Local: Select all LOCAL items this tree
  Select Peer: Select all PEER items this tree
  Save Struct to File: Save all content to file
  Show Hex: Show value by hex
  Show Decimal: Show value by decimal
  Copy to Clipboard: Copy selected items to clipboard ( Ctrl + C )
  Parse Deeply: Decode special container to extra text tree window
  Parse By ASN: Decode by ASN.1 to current tree
  Parse By Wireshark: Decode by Wireshark to extra text tree window

## Slide 10: [View] Internal Messages(2)
Popup menu in message list window
  Time Difference
  Add to Bookmark (Alt+A)
  Pre Bookmark (Alt+U)
  Next Bookmark (Alt+D)
  Filter
Parse and show message content
  Double click item to show content in bellow two windows
Sync to other view
  Double click item
Other view sync to this view
  Double click item in other view to sync to this view

## Slide 11: [View] Internal Messages(3)
Parse Deeply
  Decode the content with parser lib
  Logel tool can decode bellows:
    3G: MIB/MSG_ID_DM_UTRAN_CLASSMARK_IND
      utran_classmark
    3G: attcah_request
      ms_nw_cap, ms_ra_acc_cap
    4G: attcah_request
      ue_nw_cap, esm_message_container_contents,ms_nw_cap
    4G: attach_accept
      esm_message_container_contents
    4G: UECAPABILITYINFORMATION
    4G: ROUTING_AREA_UPDATE_REQUEST
      ms_ra_acc_cap,ms_nw_cap

## Slide 12: [View] Internal Messages(4)
Parse By ASN
  Decode the content with ASN.1 protocol
  Logel try to use ASN.1 protocol to decode the content
    If decode success, the new decoded content will show in current tree view
    If decode fail or cannot be decoded, current view no change.
    e.g.
    RRCCONNECTIONSETUPCOMPLETE
      ueCapabilityContainer

## Slide 13: [View] Internal Messages(5)
Parse By Wireshark
  Decode the content with Wireshark
  Logel tool can decode the message content by message name listed in
    \3rd\WireShark\src_3gpp.txt
  Before use this function, you need install Wireshark first, then set the install path in Option->Tool Configure->Configure.
  e.g.
    ULINFORMATIONTRANSFER
      dedicatedInfoNAS
    DLINFORMATIONTRANSFER
      dedicatedInfoNAS
    UECAPABILITYINFORMATION
      container

## Slide 14: [View] Traces
Popup Menu
  Add to Bookmark (Alt+A)
  Pre Bookmark(Alt+U)
  Next Bookmark(Alt+D)
  Export All Item To File
  Filter
  Sync to other views
  Double click the item to sync

## Slide 15: [View] Air Messages
Air Message Flow list
Popup Menu
  Add to Bookmark (Alt+A)
  Remove Bookmark (Alt+R)
  Pre Bookmark(Alt+U)
  Next Bookmark(Alt+D)
  Export All Item To File
  Sync to other views
  Double click the item to sync

## Slide 16: [View] Cell Measurements
Support 2 SIM
Three windows in this frame
  Top is LTE cell measurement
  Middle is TD/WCDMA cell measurement
  Bottom is GSM cell measurement
Popup menu
  Show value by Hex or Decimal
Open the view by the menu
  View->Common-> All Cell Measurement
  This view can be closed

## Slide 17: [View] Chart – Basic Function
Open any XXX Chart in the menu View
Clear: Pop up menu -> Clear, Clear chart
Cursor: Pop up menu -> Cursor, plus data value in the legend
Calculate Average: Pop up menu -> Average
Auto Scroll: Pop up menu -> Auto Scroll
Zoom
  Scroll mouse wheel directly
Scroll
  Hold mouse left button and move left and right in the chart field.
Draw Line : Pop up menu -> Draw Line
Draw Point : Pop up menu -> Draw Point
Show or Hide Header: Pop up menu -> Show Header
Show or Hide Legend: Pop up menu -> Show Legend
Reset Axis X to zero position: Pop up menu -> Reset Axis X
Reset Axis Y to original position: Pop up menu -> Reset Axis Y
Delay Display Value: Pop up menu -> Delay Display Value
  This is for data refresh too quick to see clearly, chart will delay to display value
Set Time Display Range: Pop up menu -> Range
View or Hide Axis Y: Pop up menu -> View Y-Axis
View or Hide Lines: Pop up menu -> View Channel
Sync with other view: Double click the chart field to sync with other views
Clear: Pop up menu -> Clear, Clear chart
Cursor: Pop up menu -> Cursor, plus data
Save chart data to user specified csv file:
Pop up menu -> Export Chart Data
Save chart data image:
Pop up menu -> Export Chart Image
Notes: Requirement ID: RS-ANA-0001

## Slide 18: [View] Chart – Average Function
Open the view by the menu
  View->xx Chart, Popup menu: Average
Function
  Display Average, Min, Max value
  Display Time Span
  User can move the average field side to select the time range to calculate average value.
Notes: Requirement ID: RS-ANA-0001

## Slide 19: [View] LTE Serving Cell Chart of SIM1/Primary
Open the view by the menu
  View->LTE> LTE Serving Cell Chart of SIM1/Primary
Function
  Display RSRP/RSRQ Ant0/1, Comb value, SINR
  Display Physical Cell ID
  Display E-ARFCN, Band
Notes: Requirement ID: RS-ANA-0001

## Slide 20: [View] LTE Serving Cell Chart of SIM2
Open the view by the menu
  View->LTE> LTE Serving Cell Chart of SIM2
Function
  Display RSRP/RSRQ Ant0/1, Comb value, SINR
  Display Physical Cell ID
  Display E-ARFCN, Band
Notes: Requirement ID: RS-ANA-0001

## Slide 21: [View] LTE Serving/Neighbor Cell Chart of SIM1/Primary
Open the view by the menu
  View->LTE> LTE Serving/Neighbor Cell Chart of SIM1 Primary
Function
  Display Serving and Neighbor cell RSRP
  Display Physical Cell ID
  Display E-ARFCN
Notes: Requirement ID: RS-ANA-0001

## Slide 22: [View] LTE Serving/Neighbor Cell Chart of SIM2
Open the view by the menu
  View->LTE> LTE Serving/Neighbor Cell Chart of SIM2
Function
  Display Serving and Neighbor cell RSRP
  Display Physical Cell ID
  Display E-ARFCN
Notes: Requirement ID: RS-ANA-0001

## Slide 23: [View] LTE PDCP Throughput Chart
Open the view by the menu
  View -> LTE -> LTE PDCP Throughput Chart
Function
  Draw PDCP throughput lines

## Slide 24: [View] LTE RLC Throughput Chart
Open the view by the menu
  View -> LTE -> LTE RLC Throughput Chart
Function
  Draw RLC throughput lines

## Slide 25: [View] LTE MAC Throughput Chart
Open the view by the menu
  View -> LTE -> LTE MAC Throughput Chart
Function
  Draw MAC throughput lines

## Slide 26: [View] LTE BSR Chart
Open the view by the menu
  View -> LTE -> LTE BSR Chart
Function
  Draw BSR Index LCG0/1/2/3 lines

## Slide 27: [View] LTE Tx/Rx Power Chart
Open the view by the menu
  View -> LTE -> LTE Tx/Rx Power Chart
Function
  Draw blow lines
    RSSI0
    RSSI1
    AGC0
    AGC1
    Pusch
    Pucch
    Prach
    SRS

## Slide 28: [View] LTE PHICH Decoding Status Chart
Open the view by the menu
  View -> LTE -> LTE PHICH Decoding Status Chart
Function
  Draw blow lines
    nPhichGroup
    nPhichSeq
    nDetPhich
    HI

## Slide 29: [View] LTE PDSCH Decoding Status Chart
Open the view by the menu
  View -> LTE -> LTE PDSCH Decoding Status Chart
Function
  Draw blow lines
    ServingCellID
    DlTmMode
    DlHARQId
    CRC
    DecRntiVal
    DecRntiType
    TbNum
    RedundancyVersion0
    RedundancyVersion1
    NewDataIndicator0
    NewDataIndicator1

## Slide 30: [View] LTE PHY DL Throughput & BLER Chart
Open the view by the menu
  View -> LTE -> LTE PHY DL Throughput & BLER Chart
Function
  Draw blow lines
    DL Throughput Rate
    DL BLER

## Slide 31: [View] LTE PHY UL Throughput & BLER Chart
Open the view by the menu
  View -> LTE -> LTE PHY UL Throughput & BLER Chart
Function
  Draw blow lines
    UL Throughput Rate
    UL BLER

## Slide 32: [View] LTE DL Number of RB/CQI/RI/DL Schedule Rate Chart
Open the view by the menu
  View -> LTE -> LTE DL Number of RB/CQI/RI/DL Schedule Rate Chart
Function
  Draw blow lines
    Number of RB
    CQI/
    RI/
    Schedule Rate

## Slide 33: [View] LTE UL Number of RB/UL Schedule Rate Chart
Open the view by the menu
  View -> LTE -> LTE UL Number of RB/UL Schedule Rate Chart
Function
  Draw blow lines
    Number of RB
    Schedule Rate

## Slide 34: [View] LTE PHY UL MCS Chart
Open the view by the menu
  View -> LTE -> LTE PHY UL MCS Chart
Function
  Draw blow lines
    MCS

## Slide 35: [View] LTE SCell State Change
Open the view by the menu
  View -> LTE -> LTE SCell State Change
Function
  Draw bellow point
    State

## Slide 36: [View] LTE IMS Configuration Timers
Open the view by the menu
  View -> LTE -> LTE IMS Configuration Timers
Function
  Show list column value bellow
    Timer
    Time

## Slide 37: [View] LTE RRC Timer
Open the view by the menu
  View -> LTE -> LTE RRC Timer
Function
  Show list column value bellow
    Type
    Timer
    Duration
    Status

## Slide 38: [View] LTE VoLTE RTP Statistics
Open the view by the menu
  View -> LTE -> LTE VoLTE RTP Statistics
Function
  Draw bellow lines
    Payload Bit Rate
    Packet Rate
    Jitter
    Packet Loss Rate

## Slide 39: [View] WCDMA Serving Cell Chart
Open the view by the menu
  View -> WCDMA -> WCDMA Serving Cell Chart
Function
  Draw blow lines
    RSCP Ant0
    RSCP Ant1
    ECNO Ant0
    ECNO Ant1
    RSSI Ant0
    RSSI Ant1

## Slide 40: [View] WCDMA Serving/Neighbor Cell Chart
Open the view by the menu
  View -> WCDMA -> WCDMA Serving Cell Chart
Function
  Draw blow lines
    RSCP Ant0
    RSCP Ant1

## Slide 41: [View] WCDMA Serving/Neighbor Cell Chart
Open the view by the menu
  View -> WCDMA -> WCDMA Serving Cell Chart
Function
  Draw blow lines
    RSCP Ant0
    RSCP Ant1

## Slide 42: [View] WCDMA RLC DL Throughput Chart
Open the view by the menu
  View -> WCDMA -> WCDMA RLC DL Throughput Chart
Function
  Draw blow lines
    RLC DL Throughput

## Slide 43: [View] WCDMA RLC UL Throughput Chart
Open the view by the menu
  View -> WCDMA -> WCDMA RLC UL Throughput Chart
Function
  Draw blow lines
    RLC UL Throughput

## Slide 44: [View] WCDMA MAC DL Throughput Chart
Open the view by the menu
  View -> WCDMA -> WCDMA MAC DL Throughput Chart
Function
  Draw blow lines
    MAC DL Throughput

## Slide 45: [View] WCDMA CQI/HSDPA BLER/HSDPA Schedule Rate Chart
Open the view by the menu
  View -> WCDMA -> WCDMA CQI/HSDPA BLER/HSDPA Schedule Rate Chart
Function
  Draw blow lines
    CQI
    HSDPA BLER
    HSDPA Schedule Rate

## Slide 46: [View] WCDMA Tx Power Chart
Open the view by the menu
  View -> WCDMA -> WCDMA Tx Power Chart
Function
  Draw blow lines
    Tx Power

## Slide 47: [View] WCDMA RLC DL/UL PDU
Open the view by the menu
  View->WCDMA> WCDMA RCL DL/UL PDU
Function
  Left view is the same as All Traces window and
  shows the filtered trace items
  Double click this item to parser the RCL PDU data
  and show them in the right window

## Slide 48: [View] GSM Serving Cell Chart
Open the view by the menu
  View -> GSM-> GSM Serving Cell Chart
Function
  Draw blow lines
    RSSI

## Slide 49: [View] GSM Serving/Neighbor Cell Chart
Open the view by the menu
  View -> GSM-> GSM Serving/Neighbor Cell Chart
Function
  Draw blow lines
    RSSI

## Slide 50: [View] GSM Rx/Tx Power Chart
Open the view by the menu
  View -> GSM-> GSM Rx/Tx Power Chart
Function
  Draw blow lines
    Rx Power
    Tx Power
    Rx Power Full Sim1
    Tx Power Sub Sim1
    Rx Power Full Sim2
    Tx Power Sub Sim2

## Slide 51: [View] GSM SNR Chart
Open the view by the menu
  View -> GSM-> GSM SNR Chart
Function
  Draw blow lines
    SNR

## Slide 52: [View] [DSP Test Point] Common DSP Test Point List
Open the view by the menu
  View -> DSP Test Point-> Common DSP Test Point List
Popup Menu
  Auto Scroll
  Show Hex (only for data column)
  Show Decimal(only for data column)
  Add to Bookmark (Alt+A)
  Remove Bookmark (Alt+R)
  Pre Bookmark (Alt+U)
  Next Bookmark (Alt+D)
  Sync to other views
  Double click the item to sync
  Search
  Step search in the toolbar to input search string
  Ctrl+G to locate the item by SN

## Slide 53: [View] [DSP Test Point] Common DSP Test Point Chart
Open the view by the menu
  View -> DSP Test Point-> Common DSP Test Point Chart
  Functions
  Control Panel: Set Address and Data filter condition. You add more conditions by Add button. To start/stop filter and drawing by Start/Stop button;
  Filter Data View: List the data filtered by conditions in the control panel
  Chart View: Draw the data

## Slide 54: [View] [DSP Test Point] LTE DSP Test Point List
Open the view by the menu
  View -> DSP Test Point-> LTE DSP Test Point List
Popup Menu
  Auto Scroll
  Show Hex (only for data column)
  Show Decimal(only for data column)
  Add to Bookmark (Alt+A)
  Remove Bookmark (Alt+R)
  Pre Bookmark (Alt+U)
  Next Bookmark (Alt+D)
  Sync to other views
  Double click the item to sync
  Search
  Step search in the toolbar to input search string
  Ctrl+G to locate the item by SN

## Slide 55: [View] [DSP Test Point] LTE DSP Test Point Chart
Open the view by the menu
  View -> DSP Test Point-> LTE DSP Test Point Chart
  Functions
  Control Panel: Set Address and Data filter condition. You add more conditions by Add button. To start/stop filter and drawing by Start/Stop button;
  Filter Data View: List the data filtered by conditions in the control panel
  Chart View: Draw the data

## Slide 56: [View] [DSP Test Point] TG DSP Test Point List
Open the view by the menu
  View -> DSP Test Point-> TG DSP Test Point List
Popup Menu
  Auto Scroll
  Show Hex (only for data column)
  Show Decimal(only for data column)
  Add to Bookmark (Alt+A)
  Remove Bookmark (Alt+R)
  Pre Bookmark (Alt+U)
  Next Bookmark (Alt+D)
  Sync to other views
  Double click the item to sync
  Search
  Step search in the toolbar to input search string
  Ctrl+G to locate the item by SN
View is same as LTE DSP Test Point List

## Slide 57: [View] [DSP Test Point] TG DSP Test Point Chart
Open the view by the menu
  View -> DSP Test Point-> TG DSP Test Point Chart
  Functions
  Control Panel: Set Address and Data filter condition. You add more conditions by Add button. To start/stop filter and drawing by Start/Stop button;
  Filter Data View: List the data filtered by conditions in the control panel
  Chart View: Draw the data
View is same as LTE DSP Test Point List

## Slide 58: [View] [DSP Test Point] AG DSP Test Point List
Open the view by the menu
  View -> DSP Test Point-> AG DSP Test Point List
Popup Menu
  Auto Scroll
  Show Hex (only for data column)
  Show Decimal(only for data column)
  Add to Bookmark (Alt+A)
  Remove Bookmark (Alt+R)
  Pre Bookmark (Alt+U)
  Next Bookmark (Alt+D)
  Sync to other views
  Double click the item to sync
  Search
  Step search in the toolbar to input search string
  Ctrl+G to locate the item by SN
View is same as LTE DSP Test Point List

## Slide 59: [View] [DSP Test Point] AG DSP Test Point Chart
Open the view by the menu
  View -> DSP Test Point-> AG DSP Test Point Chart
  Functions
  Control Panel: Set Address and Data filter condition. You add more conditions by Add button. To start/stop filter and drawing by Start/Stop button;
  Filter Data View: List the data filtered by conditions in the control panel
  Chart View: Draw the data
View is same as LTE DSP Test Point List

## Slide 60: [View] PHY Trace Chart
Open the view by the menu
  View -> Common -> PHY Trace Chart
  Functions
  Left View ：Show all parameters for draw， select some of them to draw chart.
  If cannot find trace id for parameter format string in parser, the parameter show grey
  Middle Up View : Function buttons: input part of parameter name to quick select parameter to draw chart.
  Double click type cell to change data type to sign or unsigned.
  Middle Bottom View: Show the data filtered from the PHY trace
Notice
1. Configure "PHYChartTraceFmt.xml"
a)Click Edit Configure in the menu of left view
editing as notice in this file
b)Click Reload Configure or F5 to refresh
2. Only support trace id formatted trace output
from device, not support raw string output.
3. Not support real-time drawing.
Start button enabled until log loading finished

## Slide 61: Search(1) : Ctrl+F
Ctr+F to open Find window in Internal Messages / Traces / Air Messages / Filter View 1 ~ 6)
  Top List box is used to input search key words,
    Record search history, Delete key words
    Ctrl+A to select all key words, Ctrl+Z to un-select all key words
    Click “Check All”to check or un-check all key words
    Set key words color to double click the color rect.
    Select history search keywords to click button
  Options:
    Case Sensitive
    Whole Word
    Regular Expression
    Find In Selected Items
  Search In Column
    SN, Module, Time, Content
  Search In View
    Internal Messages, Traces, Air Messages, Filter View 1 ~ 6
  Show Result List
    Append To Result List
  Close If Found
    Close this dialog if found.
Notes: Requirement ID: RS-ANA-0013

## Slide 62: Search(2): One Step Search
Input the find string in the toolbar edit box and end with Enter key to start search
Press F3 to find next
Press Shift + F3 to find previous
Only All Messages View/All Traces View/All MSG Flow View/ *DSP Test Point List support this function.

## Slide 63: Search(3): Scene Search
Open Scene search for messages
  Menu: Edit->Scene Search
  You can add or delete message/air by click new or delete button.
Introduction
  There are many scenes defined in this window
  You can quick to find the key messages

## Slide 64: Bookmark
Message/Trace/Msg Flow items can be bookmarked
Add items to bookmark or locate them by popup menu in these views (All Messages/All Trace/All Msg Flow)
Hot keys:
  Alt+A: add item to bookmark
  Alt+R: remove one bookmark
  Alt+U: go to previous bookmark
  Alt+D: go to next bookmark
Toolbar button: support above four operations
Bookmark Manager
  Open Bookmark Manager By Menu
  Edit -> Bookmark Manager
  Add notes for bookmark items
  Double click item to locate it

## Slide 65: Window Management
Layout Views
  Menu: Windows->Cascade
  Menu: Windows->Tile Horizon
  Menu: Windows->Tile Vertical
  Menu: Windows->Tile Vertical
  Menu: Windows->Minimize All
  Menu: Windows->Restore All
  Menu: Windows->Close ALL
  Menu: Windows->Arrange Icons
Remember Views Layout
  Logel Tool can remember the views' layout
Notes: Requirement ID: RS-GUI-0003
Requirement ID: RS-GUI-0004

## Slide 66: [Filter] Capture Filter
Open menu: Option->Device Configure
This will control the log output from device
  PS LOG
  DSP LOG
  AUDIO
Functions
  Show AT Command: Display the AT command
  Import: Import a customer configure
  Export: Save the configure to a xml file
  Restore: Restore to default configure
  Configure: Send control command to device
Notes: Requirement ID: RS-CAP-0001

## Slide 67: [Filter] View Filter
  Select popup menu “Filter”in All Messages/All Traces view
  This will filter what the user want to filter and show them in a new view
Notes: Requirement ID: RS-ANA-0008

## Slide 68: Tools
Menu Tool
Menu Item | Comment
Assert | Show Assert Frame, trigger device to assert
System Info | Run script to communicate with device
iLog | Get log by Bug ID and replay it
Device Control | Send some command to device
Log Data Statistics | Statistics about log size and lost rate
Check Dump File Integrity | Check dump file integrity for CP and AP
CP Dump File Transfer | Extract log data from dump, ring buffer file.
Capture W/TD/GSP IQ Log | Capture IQ Log and save them to file
Export Log From UE | Call AndroidLog2PC script to capture YLOG from device
Export Titan Files | Export Titan files for WCAMA
Export Call Setup Statistics | Output call setup statistics into csv file
Export Log Statistics By Module | Output log size statistics by module into csv file
Export Tcl Script Files | Output TCL script files for some message data
Export Network Parameters | Output network parameters into csv file
Export Network Capabilities | Output network capabilities into csv file
Show GPS Map | Show GPS map

## Slide 69: Tools-Unpack Mini Memory File
Tools->CP Dump File Transfer->Unpack Mini Memory File
  Memory File: Select the mini dump file
  Output Dir: Select a directory to save the unpacked files

## Slide 70: Tools-Extract Log From System Memory File
Tools->CP Dump File Transfer->Extract Log From System Memory File
  Memory File: Select the system dump file
  MAP File: Select the map file matched with the modem version
  AFX File: Select the afx file matched with the modem version
  Logel File: Select a save path to store the .logel file extracted.

## Slide 71: Tools-Extract Log From Mini Memory File
Tools->CP Dump File Transfer->Extract Log From System Memory File
  Memory File: Select the mini memory file unpacked from mini dump file
  Logel File: Select a save path to store the .logel file extracted.

## Slide 72: Tools- Show GPS Map
Tools->Show GPS Map, select GPS (GNSS) log file
Locate both side data by double click
You can switch GPS map provider here, and click “OK” to save settings. Default provider is Google.

## Slide 73: [Toolbar] Log data monitor
There are three circle icon to display different kinds of data output state
  1st button: PS data
  2nd button: PHY data (DSP data)
  3rd button: AGDSP data
  State:
  Initial state, not connect or not replay log
  Ready state, no data coming, this kind of data size is zero
  Data coming state, new data is coming
  No new data coming more than 5 seconds
  Show more detail information:
  Click any button of these three buttons to show detail in tip, and then click any
position to hide this tip.
Notes: Requirement ID: RS-GUI-0001

## Slide 74: [Status bar]
There are 5 column in status bar
System state and tip
Tool state and tip
Log lost statistics
Assert
Modem version
Click here to show “Log Lost Statistics”
Notes: Requirement ID: RS-GUI-0001

## Slide 75: [CMD Parameters]
Support command line start Armlogel.exe
Cmd line parameters format:
None blocking mode: Armlogel.exe –f <filepath> [options]
Blocking mode: start /WAIT Armlogel.exe –f <filepath> [options]
Format description:
Parameters | Description
-f <filepath> | Set .logel/.log/.lst file full path.
-d <ParserLibDir> | Set parser library directory.
-r [Start, [End¦+Offset]] | Set sequence number range. e.g. -r 10021,30059 -r 10021,+500 // +500 is an offset from 10021-1
Notes: Requirement ID: RS-GUI-0001

## Slide 76: [CMD Parameters]
-t [tmpdir] | Set the folder to store temporary files when playing back.
-n [WndClassName] | Set the WndClassName so that 3rd program could obtain Armlogel window handle, and send messages to it. Remarks: If 3rd program open the same Armlogel.exe, the –n option must be unique.
-p [Position] | Set the position to locate the related log data when finish playing back. If the position given overflow the SN range in –r option, nothing will be happened.
-w [min¦max¦hide] | Set the window’s show style. min: minimize max: maximize hide: hide
-q | Auto quit exe when finish playing back.
-m [yes¦no] | Whether to show error message box or not during playback if error occurs, default not to show.
Notes: Requirement ID: RS-GUI-0001

## Slide 77: [CMD Parameters]
-l [logStatisticDir] | Export log size statistics by module after log loading finished. logStatisticDir - output file’s directory Notice: If “logStatisticDir” not specified, result file will be output to the same directory as the loaded log file.
-o [m¦t¦f¦s¦w] | Indicate that export Msg/Trace/Air/DSP TP detail to txt file. It usually carries three parameters such as: -o mtf. The parameters can be freely combined. m: Msg; t: Trace; f: Air; d:DSP Test Point there are another two option: s: only export message name and .etc content but no detail message tree for Msg/Air. w: use wireshark to decode air message if export air detail message e.g. export air detailmessage using wireshark to parse -o fw e.g. only export msg no detail -o ms e.g. export DSP Test Point -o “d¦lte:0xDF9B,0xDF9c¦tg” Notice: If you don’t want to filter any air(or msg) message just use: -o fw or -o f If you want to filter some message notice that use "" : –o "f¦air:UECAPABILITYINFORMATION,RRCCONNECTIONRECONFIGURATION“ –o “m¦msg:MSG_ID_BCCH_BCH_MSG_TYPE, MSG_ID_IMS_SIP_DOWN_MSG“
Notes: Requirement ID: RS-GUI-0001

## Slide 78: THANK YOU!